## Slide 1: Green Chemistry and Engineering platform for innovation in chemical products and processes
Rene VAN BERKEL
Chief, Cleaner and Sustainable Production Unit
United Nations Industrial Development Organization
Vienna, Austria
Notes: 1

## Slide 2: Developments in Chemicals Management
Chemicals Management
Occupational Health & Safety
Community & Consumer Safety
Environmental Protection
Sustainable Development
Innovation
Efficiency
AIMS
STRATEGY
Control
New Management Frameworks
(SAICM, REACH, etc.)
New Business Models (ChL)

## Slide 3: Developments in Chemicals Management
Chemicals Management
Occupational Health & Safety
Community & Consumer Safety
Environmental Protection
Sustainable Development
Innovation
Efficiency
AIMS
STRATEGY
Control
Green Chemistry
Green Engineering
Biomimicry

## Slide 4: Green Chemistry and Engineering
Green Engineering
Green Chemistry
Aims to achieve sustainability through the application of science and technology in engineering design leading to efficient, safe and environmentally compatible industrial plants
Design, development and implementation of chemical products and processes to reduce or eliminate the use and generation of hazardous substances
Van Berkel et al (2005), Eco-Efficiency for Design and Operation of Minerals Processing Plants, Proceedings Chemeca 2005, Brisbane, Australia
Development of Green Engineering and Green Chemistry is driven by parallel sets of 12 normative sustainability principles,
which could be interpreted as high level design heuristics

## Slide 5
Anastas P. (1998), Green Chemistry: theory and practice, Oxford University Press, Oxford UK

## Slide 6: Design Heuristics
Green Chemistry | Green Engineering
Design for Waste Prevention | Design for Inherently Non-Hazardous Material and Energy Inputs and Outputs
Design for Atom Efficiency | Design for Waste Prevention
Design for Less Hazardous Chemical Synthesis | Design for Separation
Design of Safer Chemicals | Design for Maximum Energy, Space and Time Efficiency
Design for Safer Solvents and Auxiliaries | Design for “Output-Pulled” versus “Input-Pushed”
Design for Energy Efficiency | Design for Conservation of Complexity
Design for Use of Renewable Feedstocks | Design for Durability Not Immortality
Design to Reduce Derivatives | Design to Meet Need and Minimise Excess
Design for Catalysis | Design for Minimal Material Diversity
Design for Product Degradation | Design for Process Integration
Design for Real Time Analysis and Control for Pollution Prevention | Design for Performance in a Commercial After Life
Design for Inherently Safer Chemistry | Design for Renewable Material and Energy Inputs
Van Berkel (2005), Eco-Efficiency for Design and Operation of Minerals Processing Plants, Proceedings Chemeca 2005

## Slide 7: Atom Efficiency Illustrated
Cann, M et al (2000), Real World Cases in Green Chemistry, American Chemical Society, Washington DC
Atom efficiency increased from 40 to 77%
Reaction level process waste reduced from 148 to 29%
(i.e. by 80%)
1997 Winner Presidential Green Chemistry Award
Developed and commercialized by BHC, now BASF
Industrial success story

## Slide 8: Novel Solvents: Supercritical CO2
Supercritical carbon dioxide exhibits properties which are intermediate between those of gases and liquids, which make it ideal as a solvent that can easily be ‘vented off’ without evaporation or distillation and without leaving residues
The supercritical conditions are readily achievable (>31.6oC, >73 atmosphere)
Now increasingly being used on commercial scale for
  Extraction and purification of speciality chemicals and useful natural products (pharmaceuticals, caffeine etc.)
  Alternative solvent in coatings industry
  Degreasing and dry-cleaning
  Solvent for synthetic industrial processes

## Slide 9: New Reactions: Catalysis
Catalysts increase reaction yield and specificity and reduce its energy requirement and waste generation
    Nano-technology provides new possibility to design and construct effective catalysts
      For example: Fisher Tops synthesis of liquid fuels from synthesis gas produced from biomass
    Bio-catalysis is based on use of enzymes to catalyse reactions
      For example: cellulase enzymes to break down woody biomass as source for bio-ethanol production

## Slide 10: Novel Reactors: Microwaves
Microwave Technology
    Modern microwave equipment allows precise and safe control of power both in batch and continuous reactions. It enables more energy efficient heating as well as faster and cleaner chemical reactions.
    Microwaves also promote novel reaction pathways and can greatly accelerate reaction rates as a result of specific interactions.
    Applications
      Selective production and/or extraction of valuable chemicals from biomass prior to use of bulk for bio-fuel
      Widespread use in chemical discovery in pharmaceutical and related industries

## Slide 11: Hydrogen Peroxide to Propylene Oxide (HPPO)
Innovative process for production of P0
    PO is top 30 chemical intermediate – used in variety of applications
    Traditional process uses organic peroxides and produces organic byproducts, requiring disposal or recycling
    New process uses hydrogen peroxide and produces water as byproduct
    High selectivity and efficiency
        25% lower capital expenditure – no waste treatment facility required
        70-80 reduction of waste water
        35% reduction of energy
      Developed and commercialized by Dow-BASF
        First commercial plant in 2008 in Belgium
        Second commercial plant in 2011 in Thailand
2010 Winner Presidential Green Chemistry Award
Industrial success story

## Slide 12: Process Intensification
Is a engineering design strategy to adapt the process to the chemical reaction
  Doing More With Less
      Adapting size of equipment to the reaction
      Replacing large, expensive and inefficient equipment by smaller, more efficient and cheaper equipment
      Choosing the technology that best suits each process step
      Sometimes combining multiple operations in fewer aparatuses
    Multiple benefits:
      Better resource productivity and environmental performance
      Smaller, more versatile plants with lower costs
      Safer plants

## Slide 13: Eco-Efficient Plant Design
Alcoa Pinjarra Alumina Refinery Upgrade
      Additional capacity of 600 ktpa to 4.2 Mtpa – no absolute increase in GHG emissions
    Process and Utility Flow-sheet
      Maximising energy recovery, e.g. from digestion to causticiser
    Novel Unit Operations
      Seed precipitation to enhance precipitation
      Energy efficient new calciner (~ 5%)
      Regenerative Thermal Oxidisers (2*)
    Engineering Design
      Enhancements in pumping and process controls
      Re-engineering of bauxite mill
Van Berkel (2005), Eco-Efficiency for Design and Operation of Minerals Processing Plants, Proceedings Chemeca 2005
Industrial success story

## Slide 14: Biomimicry
Innovation Inspired by Nature
Biomimicry or biomimetics is the examination of nature, its models, systems, processes, and elements to emulate or take inspiration from in order to solve human problems.
14

## Slide 15: Biomimicry
Nature moves water and air using a logarithmic or exponentially growing spiral as seen in a seashell. Applying this fundamental geometry to the design of human-made rotors, reduces energy consumption by 10-85% and noise by up to 75%, in fans, mixers, pumps, turbines.
e.g. www.paxscientific.com
The lotus has a microscopically rough leaf surface that causes moisture to roll off taking attached dirt particles with it. Now microscopi- cally rough additives are added to new gene- ration paint, glass and fabric finishes, greatly reducing the need for chemical or laborious cleaning.
e.g. www.stocorp.com
www.biomimicryinstitute.org

## Slide 16: Concluding Remark
Green Chemistry and Engineering
  Proven sustainable industrial development and innovation strategy
  The desirable, but not exclusive, aim for innovation in chemical industry
    Important avenue for greening of industry and creating new green industries
Complementary nature
Control
+
Efficiency
+
Innovation
=
Green Industry Solutions

## Slide 17: Near Term Possibilities for RECPnet
Bio-plastics and bio-ethanol
    Starting from waste agricultural biomass
Supercritical Extraction with CO2
    Extraction of active ingredients (pharma, dyes, etc) from plant materials
Enzyme-technology
    Widespread opportunities for example in textile processing industry

## Slide 18: Thank You
René VAN BERKEL
Chief, Cleaner and Sustainable Production Unit
r.vanberkel(at)unido.org
www.unido.org/cp